CONDITIONS ANNEXED TO AND FORMING PART

OF LAND USE PERMIT NUMBER MV2004C0039

# Part A:		Scope of Permit

- This permit entitles Sidon International Resources Corp. to conduct the following activities:

Mineral exploration including diamond drilling and associated activities, a temporary camp, fuel storage, construction and maintenance of a winter road from Yellowknife to the Defeat Lake area.  Activities will take place in the Defeat Lake area (Latitude: 62○ 22’ N, Longitude: 113○ 42’ W).

- The Permit is issued subject to the conditions contained herein with respect to the use of land for the activities and area identified in Part A, Item 1 of this permit.

- Compliance with the terms and conditions of this permit does not absolve the Permittee from responsibility for compliance with the requirements of all applicable Federal, Territorial and Municipal legislation.

# Part B:	Definitions

“Act” means the Mackenzie Valley Resource Management Act;

“Artesian Aquifer” means a water-bearing stratum, which when encountered during drilling operations, produces a pressurized flow of groundwater that reaches an elevation above the ground surface;

“Board” means the Mackenzie Valley Land and Water Board established under Part 4 of the Mackenzie Valley Resource Management Act;

“Dogleg” means clearing a line, trail or right-of-way that is curved sufficiently so that no part of the clearing beyond the curve is visible when approached from either direction;

“Drill Waste” means all materials or chemicals, solid or liquid, associated with the drilling of boreholes and includes borehole cuttings;

“Inspector” means an Inspector designated by the Minister under the Mackenzie Valley Resource Management Act;

“Sewage” means all toilet wastes and grey water;

“Sump” means a man-made pit, trench hollow or cavity in the earth's surface used for the purpose of depositing waste material therein;

# Part C:	Conditions Applying to All Activities (the headings correspond to Subsection 26 of the Mackenzie Valley Land Use Regulations)

|  | 26(1)(a) LOCATION AND AREA |  |
| --- | --- | --- |
|  | The Permittee shall not conduct this land use operation on any lands not designated in the accepted application. | PLANS |
|  | The Permittee shall not conduct any part of the land use operation within three hundred (300) metres of any privately owned or leased land or structure. | PRIVATE PROPERTY |
|  | The Permittee shall locate all camps on gravel, sand or other durable land. Camp location should be provided to the Inspector prior to the establishment of the camp. | CAMP LOCATION |
|  | When the Permittee is drilling within one hundred (100) metres of the ordinary high water mark of a water body, they must employ a recirculating drill and ensure that cuttings do not enter any water body. | LOCATION OF DRILLSITES |
|  | The Permittee shall not construct parallel lines or roads unless authorized by the inspector. | Parallel roads |
|  | Prior to the commencement of diamond drilling the Permittee shall submit to the Inspector and the Board, proposed drill targets on a 1:50,000-scale map with coordinates and map datum. | Drill Locations |
|  | 26(1)(b) TIME |  |
|  | The Permittee's Field Supervisor shall contact an Inspector at (867) 669-2757 at least forty-eight (48) hours prior to the commencement of this land use operation. | CONTACT INSPECTOR/ BOARD |
|  | The Permittee shall advise an Inspector at least ten (10) days prior to the completion of the land use operation of (a) the plan for removal or storage of equipment and materials, and (b) when final clean-up and restoration of the land used will be completed. | REPORTS BEFORE REMOVAL |
|  | The Permittee shall provide in writing to the Inspector, at least forty-eight (48) hours prior to commencement of this land use operation, the following information: (a) person, or persons, in charge of the field operation to whom notices, orders, and reports may be served; (b) alternates; and (c) all methods for contacting the above person(s). | IDENTIFY AGENT |
|  | The Permittee shall remove all ice bridges prior to spring break-up or completion of the land use operation. | REMOVE ICE BRIDGE |
|  | The Permittee shall remove all snow fills from stream crossings prior to spring break-up or completion of the land use operation unless otherwise approved in writing by an Inspector. | REMOVE SNOW FILLS |
|  | The Permittee shall restore all sumps prior to spring break-up, unless otherwise authorized in writing by an Inspector. | SUMPS/SPRING BREAK-UP |
|  | The Board and/or Inspector reserve the right to impose closure of any area to the Permittee in periods when dangers to natural resources are severe. | CLOSURE |
|  | 26(1)(c) TYPE AND SIZE OF EQUIPMENT |  |
|  | The Permittee shall not use any equipment except of the type, size, and number that is listed in the accepted application. | ONLY APPROVED EQUIPMENT |
|  | 26(1)(d) METHODS AND TECHNIQUES |  |
|  | The Permittee shall not conduct vehicle travel in areas without snow-covered surfaces. | VEHICLE TRAVEL |
|  | The Permittee shall construct and maintain winter roads with a minimum of ten (10) centimetres packed snow at all times during this land use operation. If this cannot be done, then the Permittee shall construct Ice Roads in a manner authorized by an Inspector. | SNOW ROADS/ ICE ROADS |
|  | The Permittee shall dogleg lines, trails and rights-of-way that approach lakes, streams or public roads. | DOGLEG APPROACHES |
|  | The Permittee shall leave a buffer strip of undisturbed vegetation at least thirty (30) metres in width between cleared areas and public roads or navigable waterways. | TREE SCREEN |
|  | The Permittee shall not clear areas larger than identified in the accepted application. | MINIMIZE AREA CLEARED |
|  | The Permittee shall not erect camps or store material on the surface ice of streams. | STORAGE ON ICE |
|  | The Permittee shall not store material other than that required for immediate use on the ice surface of water bodies. | Storage on Ice |
|  | The Permittee shall remove or cut off and seal all drill casings at ground level immediately upon completion of drilling. | Removal and Sealing of Drill Casings |
|  | The Permittee shall verify that the water depth at each lake-based drill site is greater than 11 metres or frozen to the substrate and shall report this information to the Department of Fisheries and Oceans prior to the start of drilling. | LAKE DEPTH |
|  | The Permittee shall only withdraw water from lakes where the volume of water removed is not greater than 5 percent of the seasonal volume of the lake. | WATER WITHDRAWAL |
|  | 26(1)(e) TYPE, LOCATION, CAPACITY AND OPERATION OF ALL FACILITIES |  |
|  | The Permittee shall not locate any sump within one hundred (100) metres of the ordinary high water mark of any water body, unless otherwise authorized in writing by an Inspector. | SUMPS FROM WATER |
|  | The Permittee shall ensure that the land use area is kept clean at all times. | CLEAN WORK AREA |
|  | 26(1)(f) CONTROL OR PREVENTION OF PONDING OF WATER, FLOODING, EROSION, SLIDES AND SUBSIDENCE OF LAND |  |
|  | (a) The Permittee shall, where flowing water from bore holes is encountered, plug the bore hole in such a manner as to permanently prevent any further outflow of water; and (b) the artesian occurrence shall be reported to the Inspector immediately. | PLUG ARTESIAN WELLS |
|  | The land use operation shall not cause obstruction to any natural drainage. | NATURAL DRAINAGE |
|  | The Permittee shall not use any material other than water in the construction of ice bridges. | ICE BRIDGE MATERIALS |
|  | The Permittee shall not use any material other than snow in the construction of snow fills. | SNOW FILLS |
|  | The Permittee shall not allow any ice bridge to hinder the flow of water. | ICE BRIDGE |
|  | The Permittee shall prepare the site in such a manner as to prevent rutting of the ground surface. | PREVENTION OF RUTTING |
|  | The Permittee shall suspend overland travel of equipment or vehicles at the first sign of rutting. | SUSPEND OVERLAND TRAVEL |
|  | The Permittee shall not move any equipment or vehicles unless the ground surface is in a state capable of fully supporting the equipment or vehicles without rutting or gouging. | VEHICLE MOVEMENT FREEZE-UP |
|  | 26(1)(g) USE, STORAGE, HANDLING AND ULTIMATE DISPOSAL OF ANY CHEMICAL OR TOXIC MATERIAL |  |
|  | The Permittee shall not use chemicals in connection with the land use operation that were not identified in the accepted application. | APPROVAL OF CHEMICALS |
|  | The Permittee shall deposit all non-toxic drill waste into a natural depression or a sump. | DRILL WASTE |
|  | The Permittee shall remove all drill waste off ice surfaces. | Drill Waste DispoSal |
|  | The Permittee shall not allow any drilling waste to spread to the surrounding lands. | DRILL WASTE CONTAINMENT |
|  | When drilling on ice, the Permittee shall use a closed circuit drilling system with the disposal of cuttings into a land-based sump or transported to an approved disposal facility. | Drilling on Ice |
|  | The Permittee shall dispose of all combustible waste petroleum products by incineration or removal. | WASTE PETROLEUM DISPOSAL |
|  | The Permittee shall report all spills immediately to the 24 hour Spill Report Line (867) 920-8130, which is in accordance with instructions contained in "Spill Report" form N.W.T. 1752/0593. | REPORT CHEMICAL AND PETROLEUM SPILLS |
|  | 26(1)(h) WILDLIFE AND FISHERIES HABITAT |  |
|  | The Permittee shall minimize damage to wildlife and fish habitat in conducting this land use operation. | HABITAT DAMAGE |
|  | The Permittee shall not harass wildlife during this land use operation. | NO WILDLIFE HARASSMENT |
|  | The Permittee shall construct and maintain the water intake using the DFO recommended 2.54 mm fine mesh size to prevent entrainment of fish. Other dimensions must follow DFO's Freshwater Intake End-of-Pipe Fish Screen Guidelines. | PREVENT ENTRAINMENT |
|  | If migratory birds or their nesting areas, or any species at risk are encountered during the course of operations, the Permittee is to minimize all activity so as to not disturb these animals. | MINIMIZE Activity |
|  | The Permittee shall cease operations when Caribou are in the immediate vicinity of any area where work is proceeding. | caribou harrassment |
|  | During periods of caribou herd migration through the permitted area, neither drilling activities nor low-level flying shall occur, within a distance of 5 km of any caribou water crossing, until such time as the major migration has been completed. Please contact the North Slave Regional Environment and Natural Resources (ENR) Office at (867) 920-3049 for information regarding the location of water crossings and sensitive caribou habitat. | restrictions during caribou migration |
|  | 26(1)(i) STORAGE, HANDLING AND DISPOSAL OF REFUSE OR SEWAGE |  |
|  | The Permittee shall dispose of all sewage and grey water into a sump. | SEWAGE IN SUMP |
|  | The Permittee shall remove all non-combustible garbage and debris, including plastics from the land use area to a disposal site as specified in the accepted application. | REMOVE GARBAGE |
|  | The Permittee shall burn all combustible garbage and debris, except plastics, daily, in a container acceptable to an Inspector. | INCINERATION |
|  | The Permittee shall keep all garbage and debris in a covered metal container on site until disposed of. | GARBAGE CONTAINER |
|  | The Permittee shall remove all scrap metal, discarded machinery, parts, barrels and kegs, buildings and building material to an approved waste disposal facility. | REMOVE WASTE MATERIAL |
|  | 26(1)(j) PROTECTION OF HISTORICAL, ARCHAEOLOGICAL AND BURIAL SITES |  |
|  | The Permittee shall not knowingly remove, disturb, or displace any archaeological specimen or site. | DISTURBANCE OF SITE |
|  | The Permittee shall immediately cease any activity which disturbs an archaeological, historical, and/or burial site and contact the Mackenzie Valley Land and Water Board at (867) 669-0506 should an archaeological site or specimen be encountered or disturbed by any land use activity. | CONTACTS |
| 55. | The Permittee shall ensure that all persons working under authority of the permit are aware of these conditions concerning archaeological land use activity. | NOTIFICATION TO EMPLOYEES |
|  | The Permittee, while accompanied by a qualified archaeologist, an Aboriginal elder, and a translator, shall scout out archaeological, burial and cultural sites at the proposed access route and drill locations before commencement of on-land operations. | SCOUT CULTURAL SITES |
|  | No activity associated with this land use operation shall take place within one hundred (100) metres of a known and suspected archaeological, burial or sacred site. | LIMIT ACTIVITY |
|  | Prior to commencing activities the Permittee shall contact local Aboriginal organizations and the Prince of Wales Northern Heritage Centre for the precise locations and extent of recorded archaeological sites within the development area. | archaeological site data |
|  | 26(1)(k) OBJECTS AND PLACES OF RECREATIONAL, SCENIC AND ECOLOGICAL VALUE |  |
|  | 26(1)(l) SECURITY DEPOSIT |  |
|  | The Permittee shall deposit with the Minister a security deposit in the amount of $10,000 pursuant to Section 32 of the Mackenzie Valley Land Use Regulations. | SECURITY DEPOSIT |
|  | The Permittee shall be liable for any cost of damages over and above the amount of the security deposit. | LIABILITY FOR DAMAGES |
|  | All costs to remediate the area under this permit are the responsibility of the Permittee. | RESPONSIBILITY FOR REMEDIATION COSTS |
|  | 26(1)(m) FUEL STORAGE |  |
|  | The Permittee shall report in writing to an Inspector the location and quantity of all fuel caches within ten (10) days of their establishment. | REPORT FUEL LOCATION |
|  | The Permittee shall not place any fuel storage containers within one hundred (100) metres of the normal high water mark of any water body, unless otherwise authorized in writing by an Inspector. | FUEL BY STREAM |
|  | The Permittee shall locate mobile fuel facilities on land when stationary for any period of time exceeding twelve (12) hours. | FUEL ON LAND |
|  | The Permittee shall not allow petroleum products to spread to surrounding lands or into water bodies. | FUEL CONTAINMENT |
|  | The Permittee shall mark all stationary petroleum products storage facilities with flags, posts or similar devices so that they are at all times plainly visible to local vehicle travel. | MARK FUEL LOCATION |
|  | The Permittee shall seal all container outlets except the outlet currently in use. | SEAL OUTLET |
|  | The Permittee shall mark all fuel containers, including 45-gallon drums, with the Permittee's name and permit number. | MARK CONTAINERS |
|  | The Permittee shall ensure that adequate contingency plans and spill kits are in place, prior to commencement of operations, to respond to any potential spills. | SPILL RESPONSE |
|  | 26(1)(n) METHODS AND TECHNIQUES FOR DEBRIS AND BRUSH DISPOSAL |  |
|  | The Permittee shall dispose of all brush and debris cleared from trails and lines by: (a) pushing or felling the material into the adjacent forest; and (b) cutting the branches from the stems, and cutting the stems into lengths so that all parts of the trees felled lie flat on the ground surface. | BRUSH DISPOSAL |
|  | The Permittee shall complete total disposal of all debris and brush cleared prior to the expiry date of the Land Use Permit. | BRUSH DISPOSAL/ TIMING |
|  | The Permittee shall progressively complete disposal of all debris and brush. | PROGRESSIVE DISPOSAL |
|  | 26(1)(o) RESTORATION OF THE LANDS |  |
|  | The Permittee shall complete all clean-up and restoration of the lands used prior to the expiry date of this Permit. | CLEAN-UP |
|  | The Permittee shall backfill and restore all sumps prior to the expiry date of this Permit. | BACKFILL SUMPS |
|  | 26(1)(p) DISPLAY OF PERMITS AND PERMIT NUMBERS |  |
|  | The Permittee shall display a copy of this Permit in each campsite established to carry out this land use operation. | DISPLAY PERMIT |
|  | The Permittee shall keep on hand, at all times during this land use operation, a copy of the Land Use Permit. | COPY OF PERMIT |
|  | 26(1)(q) MATTERS NOT INCONSISTENT WITH THE REGULATIONS |  |
|  | The Permittee shall ensure that all persons working under the authority of the Land Use Permit are aware of and will adhere to the conditions as stated in the Land Use Permit. | NOTIFICATION TO ALL EMPLOYEES/ CONTRACTORS |
|  | The Permittee shall, while preparing the access road, make every effort to avoid covering or destroying traps or snares that may be found along these routes. | TRAPS PROTECTION |
|  | The Permittee shall restore any trails used by trappers or hunters along access routes by slashing any and all trees that may fall across these paths or trails and by removing any other obstructions such as snow piles or debris that may be pushed across the trails. | TRAILS RESTORATION |
|  | The Permittee shall submit to the Board an update of the contingency plan, for chemical and petroleum spills, if there are any changes in the operation during the life of the permit. | CONTINGENCY PLAN |
|  | The Permittee shall not conduct activities on this land use permit within 300 metres of a cabin used for traditional activities including trapping, hunting or fishing. | Avoid Cabins |